## Slide 1: Discrete Event Simulation with Python

## Slide 2: 零工式生產排程問題情境
典型的零工式行生產（job shop）系統排程環境中，其生產特性極為複雜的加工作業典型，所有工作或製令單在系統內流動有其各自的作業排程。
  每種工作或製令單有不同的來到時間（release time）與交期（due date）
  每種工作或製令單有各自的加工途程（routing）與加工時間（process time）
  主要決定工作或製令單的於各加工中心的開始時間點與投料數量
機台1
機台2
機台3
機台4
機台5
機台6
Order 1
Source
Drain
Order 2
Order 3

## Slide 3: 零工式生產排程問題
一般而言，有限產能排程問題主要可分成下列幾種：
  以「製令」為主的排程方法(Job-based Scheduling或Order-based Scheduling)：利用訂單排序法則決定訂單或製令的加工優先順序，再按順序高低逐一安排各製令的詳細作業排程。
  以「工作中心」為主的排程方法(Event-based Scheduling)：運算邏輯是利用事件導向(Event-Driven)的模擬觀念來描述製造系統的實際運作流程。
    先進先出派工法則（FIFO）：以先來到等候線的工作為優先
    最短作業時間派工法則（SPT）：以等候線中加工時間做短的作業優先
    最早交期派工法則（EDD）：以等候線中最早交期的工作為優先
    LSF, LWR,………

## Slide 4: 以「製令」為主及以「工作中心」為主的排程方法
Simulation based scheduling

## Slide 5: 離散事件模擬 (Discrete Event Simulation)
離散事件模擬模式的目的乃欲複製（reproduce）或模仿（mimic）離散事件系統所從事之活動，從而學習或瞭解系統動態行為與其績效。
模式構建乃藉著定義改變系統狀態變數的活動步驟。系統狀態變數可定義為個體數及其屬性值，資源狀態值等之變化。

## Slide 6: 事件(Event)、活動(Activity)與程序(Process)關係
程 序
活動
活動
時間
來到
事件
開始活
動事件
結束活
動事件
開始活
動事件
結束活
動事件
開始活
動事件
結束活
動事件
活動

## Slide 7
事件排程法(Event Scheduling)
在「事件排程法模擬」中，主要為描述並記錄事件點上系統狀態的變化。
模式構建的任務即在決定有那些改變系統狀態的事件，以及定義事件與事件間的邏輯關係。
模擬即以虛擬的時間推進機構將事件依時間發生先後順序負責執行其相關邏輯，從而改變系統狀態，收集相關統計資料。

## Slide 8: 事件排程法邏輯

## Slide 9: 零工式生產排程範例
1.零工式生產排程系統由三台加工機台以及個別機台前的等候暫存區（Buffer）所組成。
2.機台前的等候暫存區則可以無限容納多張製令等候加工 。
3.製令來到間隔時間：每張製令來到間隔時間也服從某種機率，有20%的機會每張製令來到的間隔時間為1分鐘，有30%的機會每張製令來到的間隔時間為2分鐘，以此類推。
4.機台加工處理時間：製令在系統內流動有其各自不同的作業途程以及加工時間，例如製令一只有經過A機器與B機器加工，且分別在這兩台機器上的加工時間為3分鐘與3分鐘 。
5.機台有空：製令馬上接受處理 ；機台正忙：製令排在等候線的最後。
6.從等候線中選擇下一張製令的規則：「製令交期越早優先加工」(EDD）。
O1
O2
O3
O4
O5
O6

## Slide 10: 零工式生產排程例的時間數據
表1. 零工式排程系統的製令數據

## Slide 11
Event type
initialize
Time
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 0
A_Complete | infinite
B_Complete | infinite
C_Complete | infinite
Dispatching | infinite
零工式生產排程範例

## Slide 12
Event type
Arrival event
Time
0
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 4
A_Complete | 5
B_Complete | 2
C_Complete | infinite
J4
J1
J3
J5
零工式生產排程範例

## Slide 13
TNOW
J1
J5
零工式生產排程範例

## Slide 14
Event type
B_complete
Time
2
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 4
A_Complete | 5
B_Complete | 6
C_Complete | 6
J4
J3
J5
J1
零工式生產排程範例

## Slide 15
TNOW
J1
J5
J5
J3
J2 release
零工式生產排程範例

## Slide 16
Event type
Arrival event
Time
4
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 7
A_Complete | 5
B_Complete | 6
C_Complete | 6
J4
J3
J5
J1
J2
零工式生產排程範例

## Slide 17
TNOW
J1
J5
J5
J3
J2 release
零工式生產排程範例

## Slide 18
Event type
A_complete
Time
5
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 7
A_Complete | 9
B_Complete | 6
C_Complete | 6
J3
J5
J2
J4
J1
零工式生產排程範例

## Slide 19
TNOW
J1
J5
J5
J3
J4
零工式生產排程範例

## Slide 20
Event type
B_complete & C_complete
Time
6
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 7
A_Complete | 9
B_Complete | 8
C_Complete | 7
J3
J5
J2
J4
J1
J5
零工式生產排程範例

## Slide 21
TNOW
J1
J5
J5
J3
J4
J5
J1
零工式生產排程範例

## Slide 22
Event type
Arrival & C_complete
Time
7
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 10
A_Complete | 9
B_Complete | 8
C_Complete | infinite
J3
J2
J5
J4
J1
J6
零工式生產排程範例

## Slide 23
TNOW
J1
J5
J5
J3
J4
J5
J1
J6 release
零工式生產排程範例

## Slide 24
Event type
B_complete
Time
8
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 10
A_Complete | 9
B_Complete | 11
C_Complete | infinite
J3
J2
J5
J4
J1
J6
Throughput : 1
零工式生產排程範例

## Slide 25
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
零工式生產排程範例

## Slide 26
Event type
A_complete
Time
9
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | 10
A_Complete | 14
B_Complete | 11
C_Complete | infinite
J3
J2
J4
J1
J6
Throughput : 1
零工式生產排程範例

## Slide 27
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
零工式生產排程範例

## Slide 28
Event type
Arrival_event
Time
10
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 14
B_Complete | 11
C_Complete | infinite
J3
J2
J4
J1
J6
Throughput : 1
J7
零工式生產排程範例

## Slide 29
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J7 release
零工式生產排程範例

## Slide 30
Event type
B_complete
Time
11
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 14
B_Complete | 13
C_Complete | 12
J3
J2
J4
J1
J6
Throughput : 1
J7
零工式生產排程範例

## Slide 31
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
零工式生產排程範例

## Slide 32
Event type
C_complete
Time
12
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 14
B_Complete | 13
C_Complete | infinite
J3
J2
J4
J1
J6
Throughput : 1
J7
零工式生產排程範例

## Slide 33
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
零工式生產排程範例

## Slide 34
Event type
B_complete
Time
13
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 14
B_Complete | 18
C_Complete | 14
J3
J2
J4
J1
J6
Throughput : 1
J7
零工式生產排程範例

## Slide 35
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
零工式生產排程範例

## Slide 36
Event type
A_complete & C_complete
Time
14
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 19
B_Complete | 18
C_Complete | infinite
J3
J2
J4
J1
J6
Throughput : 2
J7
零工式生產排程範例

## Slide 37
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
零工式生產排程範例

## Slide 38
Event type
B_complete
Time
18
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 19
B_Complete | 21
C_Complete | 20
J3
J2
J4
J6
Throughput : 2
J7
零工式生產排程範例

## Slide 39
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
零工式生產排程範例

## Slide 40
Event type
A_complete
Time
19
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 24
B_Complete | 21
C_Complete | 20
J3
J2
J4
J6
Throughput : 2
J7
零工式生產排程範例

## Slide 41
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
J3
零工式生產排程範例

## Slide 42
Event type
C_complete
Time
20
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 24
B_Complete | 21
C_Complete | 21
J3
J2
J4
J6
Throughput : 3
J7
零工式生產排程範例

## Slide 43
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
J3
J2
零工式生產排程範例

## Slide 44
Event type
B_complete & C_complete
Time
21
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 24
B_Complete | 24
C_Complete | 22
J3
J2
J4
J6
Throughput : 4
零工式生產排程範例

## Slide 45
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
J3
J2
J6
J4
零工式生產排程範例

## Slide 46
Event type
C_complete
Time
22
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | 24
B_Complete | 24
C_Complete | infinite
J3
J4
J6
Throughput : 5
零工式生產排程範例

## Slide 47
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
J3
J2
J6
J4
零工式生產排程範例

## Slide 48
Event type
A_complete & B_complete
Time
24
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | infinite
B_Complete | infinte
C_Complete | 25
J3
J4
Throughput : 5
J3
零工式生產排程範例

## Slide 49
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
J3
J2
J6
J4
J3
零工式生產排程範例

## Slide 50
Event type
C_complete
Time
25
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | infinite
B_Complete | infinte
C_Complete | 26
J3
J4
Throughput : 6
零工式生產排程範例

## Slide 51
TNOW
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
J3
J2
J6
J4
J3
J4
零工式生產排程範例

## Slide 52
Event type
C_complete
Time
26
A_Buffer
Machine A
B_Buffer
C_Buffer
Machine B
Machine C
Future Event List | 
Event type | Time
Arrival | infinite
A_Complete | infinite
B_Complete | infinte
C_Complete | infinite
J4
Throughput : 7
零工式生產排程範例

## Slide 53
J1
J5
J5
J3
J4
J5
J1
J2
J6
J1
J2
J7
J1
J2
J6
J7
J3
J2
J6
J4
J3
J4
零工式生產之排程結果

## Slide 54: 零工式生產排程手算之結果
製令編號 | 來到時間 | 完成加工時間 | 交期 | 在系統停留時間 | Lateness | Tardiness
O1 | 0 hrs | 14 hrs | 15 hrs | 14 hrs | -1 hrs | 0 hrs
O2 | 4 hrs | 21 hrs | 14 hrs | 17 hrs | 7 hrs | 7 hrs
O3 | 0 hrs | 25 hrs | 20 hrs | 25 hrs | 5 hrs | 5 hrs
O4 | 0 hrs | 26 hrs | 24 hrs | 26 hrs | 2 hrs | 2 hrs
O5 | 0 hrs | 8 hrs | 10 hrs | 8 hrs | -2 hrs | 0 hrs
O6 | 7 hrs | 22 hrs | 16 hrs | 15 hrs | 6 hrs | 6 hrs
O7 | 10 hrs | 20 hrs | 20 hrs | 10 hrs | 0 hrs | 0 hrs

## Slide 55: 事件排程法 with Python

## Slide 56: 物件導向程式設計風格
物件導向目的
  可維護性：要更新時，只需改要改的東西
  可複用性：可以後來重複使用
  可擴展性：如果需增加條件，只需要另外再增加就可以
  靈活性：可透過條件改變滿足需求

## Slide 57: 事件排程法邏輯
事件類別：
來到事件 ----- Source
派工事件(開始加工事件) ----- Machine
結束加工事件 ----- Machine

## Slide 58: Class類別 & 物件應用
本例包含之 class 類別：
  Order
  Factory
  Source
  Machine

## Slide 59: Class類別 & 物件應用
Order:
  Attribute:
    ID
    due date
    routing
    progress
    processing time
  Statistics:
    arrival time
    finish time
先設定好需收集的統計
紀錄每張製令的來到時間, 完成時間
Input

## Slide 60: Class類別 & 物件應用
Source:
  Attribute:
    order information
  Statistics:
    output
  Method:
    order arrival(arrival_event)
此物件的屬性含所有製令資訊(表1)
此站需紀錄投料數量
Method 執行各製令的來到事件
Input

## Slide 61: Class類別 & 物件應用
Machine:
  Attribute:
    ID
    dispatching rule
    state
    buffer
    working space
  Method:
    start processing
    end processing
在此物件的屬性中建立兩個list ，一作機台前之暫存區(buffer)，用以存放系統之半成品，另一個為機台的working space。
機台執行開始加工與結束工作事件。
Input

## Slide 62: Class類別 & 物件應用
Factory:
  Attribute:
    order information
    dispatching rule
    (future) event list
  Statistics:
    系統產出
    各製令模擬結果
  Method:
    建立Factory
    依event type執行事件
    執行下次事件直到stop
    更新統計量
Input

## Slide 63: Class類別 & 物件應用
Factory:
  __build__(): 設定建造一個工廠所需的物件，例如：一個Source、三部機台。
  需提供更新order statistic的功能, 以計算平均flow time、lateness、tardiness
  使用gantt_plot，繪製排程結果之甘特圖。
  Components:
    Source
    Machine A
    Machine B
    Machine C

## Slide 64
python語言之模擬模式構建
主程式:
讀取製令資訊表，將製令依照來到時間排序
選擇適合的派工法則
建立欲模擬之生產系統，並開始事件排程法
輸出排程結果與系統績效

## Slide 65
python語言之模擬模式構建
離散事件排程法:

## Slide 66
python語言之模擬模式構建
來到事件:
從資訊表讀取將來到之製令資訊
(ID, routing, DD etc.)
並生成Order
更新投料數量
預排下一張製令的來到事件
判斷來到之製令的第一站為哪部機台，送往其暫存區，並執行以下邏輯：
IF <機台有空> {
<安排派工事件> }
ELSE {
<製令在暫存區等待> }

## Slide 67
python語言之模擬模式構建
派工事件:
待所有工件都來到後，各機台執行開始加工事件，並更新 future event list

## Slide 68
python語言之模擬模式構建
開始加工事件:
紀錄機台的加工資訊，以繪製甘特圖
預排該機台的結束加工事件與更新製令的加工進度
IF<機台閒置>
IF<暫存區有製令待加工>
{
<依派工法則選擇製令>
<將該製令從buffer移除>
<將該製令加入工作區>
<讀取製令之加工時間>
<更改機台狀態為忙碌>
}

## Slide 69
python語言之模擬模式構建
結束加工事件:
<工作區移除完成加工之製令>
<更改機台狀態為閒置>
IF<該製令完成所有加工進度>
{
<更新系統產出量>
<計算製令之加工結果>
}
ELSE
{
<判斷製令的下一加工站>
<將其送往目標機台暫存區>
}
<安排派工事件>
<更新future event list>